## Slide 1: TCP/IP
EN.600.444/644
Fall 2019
Dr. Seth James Nielson

## Slide 2: IPv4 Protocol
Layer 3 Protocol
Handles fragmentation and reassembly
  Assumed that across multiple LANS, multiple MAC protocols
  Each MAC protocol might have its own MTU
Also, of course, includes the global IP address
  Kind of global…

## Slide 3: IPV4 Header

## Slide 4: IPv4 Header FIELDS
Version – 0100 (binary 4)
Header Length – Length of header in 4-byte increments
Total Length – Size of header and data in bytes (max 65535)
Identification – for recognizing fragments
Flags
  Reserved. Always 0
  Don’t fragment
  More fragments

## Slide 5: More IPV4 Header Fields
Fragment Offset – Offset in original datagram
TTL – Counter to prevent infinite routing
Protocol – Information about upper layer (17=UDP, 6=TCP)
Header Checksum
  Recomputed each hop (because of TTL changes)
  Checksum field itself always presumed to be 0

## Slide 6: Original ToS

## Slide 7: Differentiated Services

## Slide 8: ECN
Explicit Congestion Notification
When enabled, indicates congestion without dropping
Not all hardware/software supports ECN

## Slide 9: IPV4 Addresses
IPv4 Addresses are a.b.c.d where each is between 0-255
In actuality, just a 32-bit number (“four octets”)
  192.0.2.235
  3221226219
  0xC00002EB (0xC0.0x00.0x02.0xEB)
Private Networks:
  10.0.0.0
  172.16.0.0
  192.168.0.0

## Slide 10: Fragmentation
If packet size > MTU, and DNF is 0
  Each fragment gets its own size
  Each fragment except the last gets MF set to 1
  Fragment offset is location in the original packet
  Identification field is unique identifier of original datagram
Reassembly
  Use src, dst, protocol, and identification to identify fragments
  Use offset to store data in reassembly buffer
  Use MF = 0 to recognize end of reassembly

## Slide 11: Fragmentation Issues
IPv4 Fragmentation had security issues
  IP Fragmentation Overlap (overwrite a fragment)
  Buffer full (too many incomplete fragments)
  Fragment overrun
  (Note that most of these are DoS, but some evasion)

## Slide 12: IPv6

## Slide 13: IPV6 Header Fields
Version = 0110 (binary 6)
Traffic Class: Differentiated services plus ECN
Flow label: Hint for multiple outbound paths
Payload length: Includes extension headers, in bytes
Next header: Type of next extension or transport header
Hop limit: Decrement by 1, discard if 0

## Slide 14: Extension Headers
IPv6 is always 40 bytes for main header
Can have additional headers:

## Slide 15: Common Extension Headers

## Slide 16: IPV6 Fragmentation
To deal with IPv4 Frag issues, ONLY SENDER can frag in IPv6
Ergo, sender must know smallest MTU of path!
Path MTU Discovery (PMTUD)
  If too big, send an ICMPv6 “packet too big” to sender
Otherwise, max IPv6 packet size is 1,280 bytes.
Uses a fragmentation extension header
  Identification
  MF, etc

## Slide 17: IPv6 Frag Problems
Studies from 2014-present indicate IPv6 fragmentation fails
About one-third of IPv6 hosts could not receive frags
Many are concluding that IPv6 fragmentation is deprecated
Maximum IPv6 packet size between 1280 and 1350
See,
  https://blog.apnic.net/2016/05/19/fragmenting-ipv6/
  https://labs.apnic.net/?p=1033

## Slide 18: TCP Protocol
Layer 4 Protocol
Multiplexing (ports)
Reliable Delivery (ack/resend)
Congestion control
Units called *segments*

## Slide 19: Review
Ethernet frame
IP packet
TCP segment

## Slide 20: TCP Header

## Slide 21: TCP Header FIELDS
Source Port, Destination Port for multiplexing
Sequence Number of the first data byte
Acknowledgement Number of next expected seq. no.
Hlen number of 32-byte words in the TCP header
Window number of bytes willing to receive
Checksum over the header and data

## Slide 22: TCP Flags
URG The URGENT POINTER field contains valid data
ACK The acknowledgement number is valid
PSH The receiver should pass this data to the application as soon as possible
RST Reset the connection
SYN Synchronize sequence numbers to initiate a connection.
FIN Sender is finished sending data

## Slide 23: ECN Flags added in RFC 3168
Standard in 2001

## Slide 24: TCP Flags (Cont)
CWR – Acknowledges that congestion notification received
ECN – indicates congestion notification via IP layer
  (NOTE! Requires ECN capable IP layer!)
  Sent until CWR received
Only used if negotiated using TCP options during handshake

## Slide 25: Optional NS flag

## Slide 26: One-Bit Nonce
NS is a parity bit used to catch changes to a packet
Because it’s only one bit, a cheater can guess it 50% right
But, over repeated trials (frequent congestion) will get caught

## Slide 27: TCP Options
Header can be “extended” with options
Each option can have up to three fields:
  Option Type (1 byte)
  Option Length (1 byte)
  Option data (variable)
Examples include
  Selective acknowledgement
  ECN

## Slide 28: TCP Sequence Numbers
TCP header has a value for seq num and ack num every time
SYN Sequence Number random between 0-4,294,967,295
SYN Ack Num should be 0 (but any value should be ignored)
SYN-ACK Seq Num also random
SYN-ACK Ack Num is SYN Seq Num + 1
(SYN-ACK) ACK Seq Num is SYN Seq Num + 1
(SYN-ACK) ACK Ack Num is SYN-ACK Seq Num + 1

## Slide 29: Data Sequence Numbers
Technically, there is only one packet type in TCP
Flags simply indicate how the values can be used
Sequence number is set every time
But only increased by the length of the data
(or increased by +1 for SYN and FIN)
Ack field indicates that the ACK number is valid

## Slide 30: Wireshark Trace

## Slide 31: TCP Shutdown

## Slide 32: Security
Obviously, TCP is not designed with security in mind
  No confidentiality!
  No authentication!
  No integrity (checksum is not cryptographic)
No secure availability either!
  End any connection with RST